## Slide 1: MAIN-LINE AUTOMATION PROPOSAL
FLOWCHART
NOTES:
Purpose of Automation is:
Traceability
History of Unit Production
Automated PIT
Record Data
Summary of Defects or Issues
Summary of all Materials needed for production

## Slide 2: LINE 1
Notes:
1. Every decision should scan serial number first
2. If no good from previous scan, error will occur if scanned as good in the next one, only the scanner that tagged the unit as no good can change to good
3. Red Highlight means repair entry
4. Blue Highlight means there is data to be recorded (use of equipment)

## Slide 3
START
SFIS 1: FAN MOTOR & COMPRESSOR RECORDING and CHECKING
INSPECTION 1: AIRTIGHT TEST
SCAN FOR MODEL THAT WILL BE IN PRODUCTION
SFIS 2: GAS CHARGING
SFIS 4: CONTROL BOARD & OUTDOOR PCB
INSPECTION 2: WIRING AND CONSTRUCTION INSPECTION
INSPECTION : RUNNING INSPECTION
INSPECTION 4: VIBRATION TEST
INSPECTION 5: FINAL INSPECTION
SFIS 5: PACKAGING
SFIS 3: INDOOR CONTROL BOARD
END
LINE AUTOMATION PROPOSAL
NOTE: A unit cannot proceed to the next step if it is not scanned/approved in the previous one
IS THE UNIT J-CHASSIS HK?
YES
NO

## Slide 4
START OF SFIS 1
SCANNING OF MODEL & SERIAL NUMBER
IS IT THE CORRECT COMPRESSOR TO BE USED?
1X1 SCANNING OF COMPRESSOR
END OF SFIS 1
MODEL & SERIAL # RECORDED
COMPRESSOR PART NUMBER & SERIAL NUMBER RECORDED
B
IS IT THE CORRECT FAN MOTOR TO BE USED?
1 BY 1 SCANNING OF FAN MOTOR
FAN MOTOR PART NUMBER & SERIAL NUMBER RECORDED
SCANNING OF MODEL & SERIAL NUMBER
C
YES
NO
NO
YES
PRINT: “INCORRECT”
CHANGE THE FAN MOTOR
PRINT: “INCORRECT”
CHANGE THE COMPRESSOR

## Slide 5
START OF FIRST INSPECTION (AIRTIGHT TEST)
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
C
IS THE UNIT INVERTER?
NO
YES
TEST IF EXPANSION VALVE IS OPEN
D
CONDUCT OF VACUUMING
IS THE UNIT VACUUMED?
SET LIGHT ALARM
YES
NOT YET
END OF FIRST INSPECTION (AIRTIGHT TEST)
IS THE EXPANSION VALVE FULLY OPENED?
AIRTIGHT TEST
ARE THERE LEAKS? CLOGS?
YES
NO
YES

## Slide 6
START OF SFIS 2
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 2
MODEL & SERIAL # RECORDED
D
IS IT THE CORRECT GAS CHARGE FOR THE RUNNING MODEL?
GAS CHARGING
GAS CHARGE RECORDED
E
YES
NO
PRINT: “INCORRECT”

## Slide 7
START OF SFIS 4
END OF SFIS 4
E
IS IT AN INVERTER MODEL?
1 BY1 SCANNING OF CONTROL BOARD COMPLETE
CONTROL BOARD SERIAL NUMBER RECORDED
YES
NO
PRINT: “INCORRECT”
IS IT THE CORRECT CONTROL BOARD COMPLETE?
1 X 1 SCANNING OF OUTDOOR PCB
IS IT THE CORRECT OUTDOOR PCB?
CHANGE THE OUTDOOR PCB
PRINT: “INCORRECT”
CHANGE THE CONTROL BOARD
OUTDOOR PCB SERIAL NUMBER RECORDED
YES
NO
YES
NO
G
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
F

## Slide 8
START OF SFIS 3
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 3
MODEL AND ITS SAFETY PARTS
SCANNING OF SAFETY PARTS
SAFETY PARTS CHECKED/RECORDED
NO
IS IT THE CORRECT SAFETY PART(s) FOR THE RUNNING MODEL?
PRINT: “INCORRECT”
CHANGE THE SAFETY PART(s)
YES
E
ASSEMBLY OF CONTROL BOARD COMPLETE
SCANNING OF CONTROL BOARD COMPLETE
COUNT ON HOW MANY CONTROL BOARD COMPLETE WAS ASSEMBLED
F
CHECKING OF PROGRAM

## Slide 9
START OF INSPECTION 2 (WIRING AND CONSTRUCTION)
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 2
MODEL & SERIAL # RECORDED
G
DOES THE UNIT HAVE THE CORRECT SEQUENCE OF WIRINGS?
INSPECTION OF WIRING
SCAN AND RECORD: GOOD
H
YES
NO
SCAN “NO GOOD”
REWORK WIRING

## Slide 10
START OF INSPECTION 3 (RUNNING INSPECTION)
SCANNING OF MODEL & SERIAL NUMBER
END OF INSPECTION 3
MODEL & SERIAL # RECORDED
H
IS THE UNIT NOT NOISY (COMPRESSOR, AND FAN MOTOR)? IS THE AIRSWING FUNCTIONING? ARE THE EVAPORATOR AND CONDENSER TUBES COLD OR HOT? DOES THE UNIT HAVE THE RIGHT PROGRAM?
LEAK TEST
R
RECORD LEAK TEST RESULT
RECORD VALUES AND GOOD
PUNCTURE TEST
DOES THE UNIT PASSED BOTH LEAK TEST AND PUNCTURE TEST? IS THERE TOUCHING MATERIALS? MISALIGNED TUBES? LACKING PARTS?
CONSTRUCTION INSPECTION
SCAN “NO GOOD”
RUNNING INSPECTION
CHARACTERISTIC TEST
ARE THE VALUES WITHIN THE RANGE?
RECORD CHARAC TEST VALUES
NO GOOD
I
SCAN “NO GOOD”
R
R
PROGRAM CHECK/KNOB CHECK
NO
YES
YES
NO
NO
YES

## Slide 11
START OF INSPECTION 3
(VIBRATION TEST)
SCANNING OF MODEL & SERIAL NUMBER
END OF INSPECTION 3
MODEL & SERIAL # RECORDED
I
DOES THE UNIT PASS THE VIBRATION TEST?
VIBRATION TEST
SCAN GOOD
J
YES
NO
SCAN NO GOOD
RESULT RECORDED
R

## Slide 12
START OF INSPECTION 4
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
J
IS THE SERIAL AND MODEL NUMBER THE SAME?
PUNCTURE AND INSULATION TEST
R
RECORD INSULATION TEST VALUES
DOES THE UNIT HAVE THE CORRECT MODEL LABEL AND BADGE? CORRECT MANUAL COMPLETE AND FRONT GRILLE?
PRINT “ERROR”
ARE THE VALUES WITHIN THE RANGE? DOES THE UNIT PASSED IN THE PUNCTURE TEST?
NO GOOD
K
SCAN “GOOD”
VISUAL INSPECTION
SCANNING OF MODEL & SERIAL NUMBER IN NAME PLATE AND BARCODE
SCAN AND RECORD: GOOD
END OF INSPECTION 4
SCAN NO GOOD
R
NO
YES
NO
YES
NO
YES

## Slide 13
START OF SFIS 5
END OF SFIS 5
1 BY 1 SCANNING OF CC CASE
CC CASE SERIAL NUMBER RECORDED
NO
IS IT THE CORRECT CC CASE FOR THE RUNNING MODEL? ARE THERE NO DAMAGES IN THE CC CASE?
IF INCORRECT CC CASE: PRINT “ERROR”
IF THERE ARE DAMAGES: SCAN NO GOOD, DAMAGED CC CASE
CHANGE THE CC CASE
YES
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
K
VISUAL INSPECTION
ARE ALL THE ACCESSORIES COMPLETE? (MANUAL, FRONT GRILLE, ETC. (DIFFERENT PER MODEL)
SCAN NO GOOD: LACKING
COMPLETION OF LACKING ACCESSORIES
YES
NO

## Slide 14: LINE 2
Notes:
1. Every decision should scan serial number first
2. If no good from previous scan, error will occur if scanned as good in the next one, only the scanner that tagged the unit as no good can change to good

## Slide 15
START
SFIS 1: FAN MOTOR & COMPRESSOR RECORDING and CHECKING
INSPECTION 1: AIRTIGHT TEST
SCAN FOR MODEL THAT WILL BE IN PRODUCTION
SFIS 2: GAS CHARGING
SFIS 4: CONTROL BOARD & OUTDOOR PCB
INSPECTION 2: WIRING AND CONSTRUCTION INSPECTION
INSPECTION : RUNNING INSPECTION
INSPECTION 4: VIBRATION TEST
INSPECTION 5: FINAL INSPECTION
SFIS 5: PACKAGING
SFIS 3: INDOOR CONTROL BOARD
END
LINE AUTOMATION PROPOSAL
NOTE: A unit cannot proceed to the next step if it is not scanned/approved in the previous one
IS THE UNIT J-CHASSIS HK?
YES
NO

## Slide 16
START OF SFIS 1
SCANNING OF MODEL & SERIAL NUMBER
IS IT THE CORRECT COMPRESSOR TO BE USED?
1X1 SCANNING OF COMPRESSOR
END OF SFIS 1
MODEL & SERIAL # RECORDED
COMPRESSOR PART NUMBER & SERIAL NUMBER RECORDED
B
IS IT THE CORRECT FAN MOTOR TO BE USED?
1 BY 1 SCANNING OF FAN MOTOR
FAN MOTOR PART NUMBER & SERIAL NUMBER RECORDED
SCANNING OF MODEL & SERIAL NUMBER
C
YES
NO
NO
YES
PRINT: “INCORRECT”
CHANGE THE FAN MOTOR
PRINT: “INCORRECT”
CHANGE THE COMPRESSOR

## Slide 17
START OF FIRST INSPECTION (AIRTIGHT TEST)
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
C
IS THE UNIT INVERTER?
NO
YES
TEST IF EXPANSION VALVE IS OPEN
D
CONDUCT OF VACUUMING
IS THE UNIT VACUUMED?
SET LIGHT ALARM
YES
NOT YET
END OF FIRST INSPECTION (AIRTIGHT TEST)
IS THE EXPANSION VALVE FULLY OPENED?
AIRTIGHT TEST
ARE THERE LEAKS? CLOGS?
YES
NO
YES

## Slide 18
START OF SFIS 2
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 2
MODEL & SERIAL # RECORDED
D
IS IT THE CORRECT GAS CHARGE FOR THE RUNNING MODEL?
GAS CHARGING
GAS CHARGE RECORDED
E
YES
NO
PRINT: “INCORRECT”

## Slide 19
START OF SFIS 4
END OF SFIS 4
E
IS IT AN INVERTER MODEL?
1 BY1 SCANNING OF CONTROL BOARD COMPLETE
CONTROL BOARD SERIAL NUMBER RECORDED
YES
NO
PRINT: “INCORRECT”
IS IT THE CORRECT CONTROL BOARD COMPLETE?
1 X 1 SCANNING OF OUTDOOR PCB
IS IT THE CORRECT OUTDOOR PCB?
CHANGE THE OUTDOOR PCB
PRINT: “INCORRECT”
CHANGE THE CONTROL BOARD
OUTDOOR PCB SERIAL NUMBER RECORDED
YES
NO
YES
NO
G
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
F

## Slide 20
START OF SFIS 3
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 3
MODEL AND ITS SAFETY PARTS
SCANNING OF SAFETY PARTS
SAFETY PARTS CHECKED/RECORDED
NO
IS IT THE CORRECT SAFETY PART(s) FOR THE RUNNING MODEL?
PRINT: “INCORRECT”
CHANGE THE SAFETY PART(s)
YES
E
ASSEMBLY OF CONTROL BOARD COMPLETE
SCANNING OF CONTROL BOARD COMPLETE
COUNT ON HOW MANY CONTROL BOARD COMPLETE WAS ASSEMBLED
F

## Slide 21
START OF INSPECTION 2 (WIRING AND CONSTRUCTION)
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 2
MODEL & SERIAL # RECORDED
G
DOES THE UNIT HAVE THE CORRECT SEQUENCE OF WIRINGS?
INSPECTION OF WIRING
SCAN AND RECORD: GOOD
H
YES
NO
SCAN “NO GOOD”
REWORK WIRING
INSPECTION OF CONSTRUCTION
IS THERE TOUCHING MATERIALS? MISALIGNED TUBES? LACKING PARTS?
YES
SCAN: “NO GOOD”
REWORK WIRING
SCAN AND RECORD: GOOD
NO

## Slide 22
START OF INSPECTION 3 (RUNNING INSPECTION)
SCANNING OF MODEL & SERIAL NUMBER
END OF INSPECTION 3
MODEL & SERIAL # RECORDED
H
IS THE UNIT NOT NOISY (COMPRESSOR, AND FAN MOTOR)? IS THE AIRSWING FUNCTIONING? ARE THE EVAPORATOR AND CONDENSER TUBES COLD OR HOT?
LEAK TEST
R
RECORD LEAK TEST RESULT
SCAN AND RECORD: GOOD
PUNCTURE TEST
DOES THE UNIT PASSED BOTH LEAK TEST AND PUNCTURE TEST? DOES THE UNIT HAVE THE RIGHT PROGRAM?
PROGRAM CHECKING/KNOB CHECK
SCAN “NO GOOD”
RUNNING INSPECTION
CHARACTERISTIC TEST
ARE THE VALUES WITHIN THE RANGE?
RECORD CHARAC TEST VALUES
SCAN “NO GOOD”
I
SCAN “NO GOOD”
R
R
NO
NO
NO
YES
YES
YES

## Slide 23
START OF INSPECTION 3
(VIBRATION TEST)
SCANNING OF MODEL & SERIAL NUMBER
END OF INSPECTION 3
MODEL & SERIAL # RECORDED
I
DOES THE UNIT PASS THE VIBRATION TEST?
VIBRATION TEST
SCAN GOOD
J
YES
NO
SCAN NO GOOD
RESULT RECORDED
R

## Slide 24
START OF INSPECTION 4
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
J
IS THE SERIAL AND MODEL NUMBER THE SAME?
PUNCTURE AND CHARACTERISTIC TEST
R
RECORD CHARAC TEST VALUES
DOES THE UNIT HAVE THE CORRECT MODEL LABEL AND BADGE? CORRECT MANUAL COMPLETE AND FRONT GRILLE?
PRINT “ERROR”
ARE THE VALUES WITHIN THE RANGE? DOES THE UNIT PASSED IN THE PUNCTURE TEST?
SCAN “NO GOOD”
K
SCAN “GOOD”
VISUAL INSPECTION
SCANNING OF MODEL & SERIAL NUMBER IN NAME PLATE AND BARCODE
SCAN AND RECORD: GOOD
END OF INSPECTION 4
SCAN NO GOOD
R
NO
NO
NO
YES
YES
YES

## Slide 25
START OF SFIS 5
END OF SFIS 5
1 BY 1 SCANNING OF CC CASE
CC CASE SERIAL NUMBER RECORDED
NO
IS IT THE CORRECT CC CASE FOR THE RUNNING MODEL? ARE THERE NO DAMAGES IN THE CC CASE?
IF INCORRECT CC CASE: PRINT “ERROR”
IF THERE ARE DAMAGES: SCAN NO GOOD, DAMAGED CC CASE
CHANGE THE CC CASE
YES
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
K
VISUAL INSPECTION
ARE ALL THE ACCESSORIES COMPLETE? (MANUAL, FRONT GRILLE, ETC. (DIFFERENT PER MODEL)
SCAN NO GOOD: LACKING
COMPLETION OF LACKING ACCESSORIES
YES
NO

## Slide 26: LINE 3
Notes:
1. Every decision should scan serial number first
2. If no good from previous scan, error will occur if scanned as good in the next one, only the scanner that tagged the unit as no good can change to good

## Slide 27
START
SFIS 1: FAN MOTOR & COMPRESSOR RECORDING and CHECKING
INSPECTION 1: AIRTIGHT TEST
SCAN FOR MODEL THAT WILL BE IN PRODUCTION
SFIS 2: GAS CHARGING
INSPECTION 2: WIRING AND CONSTRUCTION INSPECTION
INSPECTION : RUNNING INSPECTION
INSPECTION 5: FINAL INSPECTION
SFIS 5: PACKAGING
SFIS 3: INDOOR CONTROL BOARD
END
LINE AUTOMATION PROPOSAL
NOTE: A unit cannot proceed to the next step if it is not scanned/approved in the previous one
SFIS 4: CONTROL BOARD MOUNTING
IS IT YWA?
CONSTRUCTIONAND RUNNING INSPECTION

## Slide 28
START OF SFIS 1
SCANNING OF MODEL & SERIAL NUMBER
IS IT THE CORRECT COMPRESSOR TO BE USED?
1X1 SCANNING OF COMPRESSOR
END OF SFIS 1
MODEL & SERIAL # RECORDED
COMPRESSOR PART NUMBER & SERIAL NUMBER RECORDED
B
IS IT THE CORRECT FAN MOTOR TO BE USED?
1 BY 1 SCANNING OF FAN MOTOR
FAN MOTOR PART NUMBER & SERIAL NUMBER RECORDED
SCANNING OF MODEL & SERIAL NUMBER
C
YES
NO
NO
YES
PRINT: “INCORRECT”
CHANGE THE FAN MOTOR
PRINT: “INCORRECT”
CHANGE THE COMPRESSOR

## Slide 29
START OF SFIS 4
END OF SFIS 4
E
IS IT AN INVERTER MODEL?
1 BY1 SCANNING OF CONTROL BOARD COMPLETE
CONTROL BOARD SERIAL NUMBER RECORDED
YES
NO
PRINT: “INCORRECT”
IS IT THE CORRECT CONTROL BOARD COMPLETE?
1 X 1 SCANNING OF OUTDOOR PCB
IS IT THE CORRECT OUTDOOR PCB?
CHANGE THE OUTDOOR PCB
PRINT: “INCORRECT”
CHANGE THE CONTROL BOARD
OUTDOOR PCB SERIAL NUMBER RECORDED
YES
NO
YES
NO
G
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
F

## Slide 30
START OF SFIS 3
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 3
MODEL AND ITS SAFETY PARTS
SCANNING OF SAFETY PARTS
SAFETY PARTS CHECKED/RECORDED
NO
IS IT THE CORRECT SAFETY PART(s) FOR THE RUNNING MODEL?
PRINT: “INCORRECT”
CHANGE THE SAFETY PART(s)
YES
E
ASSEMBLY OF CONTROL BOARD COMPLETE
SCANNING OF CONTROL BOARD COMPLETE
COUNT ON HOW MANY CONTROL BOARD COMPLETE WAS ASSEMBLED
F

## Slide 31
START OF FIRST INSPECTION (AIRTIGHT TEST)
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
C
IS THE UNIT INVERTER?
NO
YES
TEST IF EXPANSION VALVE IS OPEN
D
CONDUCT OF VACUUMING
IS THE UNIT VACUUMED?
SET LIGHT ALARM
YES
NOT YET
END OF FIRST INSPECTION (AIRTIGHT TEST)
IS THE EXPANSION VALVE FULLY OPENED?
AIRTIGHT TEST
ARE THERE LEAKS? CLOGS?
YES
NO
YES

## Slide 32
START OF SFIS 2
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 2
MODEL & SERIAL # RECORDED
D
IS IT THE CORRECT GAS CHARGE FOR THE RUNNING MODEL?
GAS CHARGING
GAS CHARGE RECORDED
E
YES
NO
PRINT: “INCORRECT”

## Slide 33
START OF INSPECTION 2 (WIRING AND CONSTRUCTION)
SCANNING OF MODEL & SERIAL NUMBER
END OF SFIS 2
MODEL & SERIAL # RECORDED
G
DOES THE UNIT HAVE THE CORRECT SEQUENCE OF WIRINGS?
INSPECTION OF WIRING
SCAN AND RECORD: GOOD
H
YES
NO
SCAN “NO GOOD”
REWORK WIRING
INSPECTION OF CONSTRUCTION
IS THERE TOUCHING MATERIALS? MISALIGNED TUBES? LACKING PARTS?
YES
SCAN: “NO GOOD”
REWORK WIRING
SCAN AND RECORD: GOOD
NO
FOR YWA

## Slide 34
START OF INSPECTION 3 (RUNNING INSPECTION)
SCANNING OF MODEL & SERIAL NUMBER
END OF INSPECTION 3
MODEL & SERIAL # RECORDED
H
IS THE UNIT NOT NOISY (COMPRESSOR, AND FAN MOTOR)? IS THE AIRSWING FUNCTIONING? ARE THE EVAPORATOR AND CONDENSER TUBES COLD OR HOT? IS THE PROGRAM RIGHT? ARE THE KNOBS WORKING?
R
SCAN AND RECORD: GOOD
PUNCTURE TEST
DOES THE UNIT THE TEST? DOES THE UNIT HAVE THE RIGHT PROGRAM?
SCAN “NO GOOD”
RUNNING INSPECTION
CHARACTERISTIC TEST
ARE THE VALUES WITHIN THE RANGE?
RECORD CHARAC TEST VALUES
SCAN “NO GOOD”
I
SCAN “NO GOOD”
R
R
NO
NO
NO
YES
YES
YES
For YWA
PROGRAM CHECKING/KNOB CHECK
LEAK TEST
RECORD LEAK TEST RESULT

## Slide 35
START OF INSPECTION 3 (RUNNING INSPECTION)
SCANNING OF MODEL & SERIAL NUMBER
END OF INSPECTION 3
MODEL & SERIAL # RECORDED
H
IS THE UNIT NOT NOISY (COMPRESSOR, AND FAN MOTOR)? IS THE AIRSWING FUNCTIONING? ARE THE EVAPORATOR AND CONDENSER TUBES COLD OR HOT? IS THE PROGRAM RIGHT? ARE THE KNOBS WORKING?
R
SCAN AND RECORD: GOOD
PUNCTURE TEST
DOES THE UNIT THE TEST? DOES THE UNIT HAVE THE RIGHT PROGRAM?
SCAN “NO GOOD”
RUNNING INSPECTION
CHARACTERISTIC TEST
ARE THE VALUES WITHIN THE RANGE?
RECORD CHARAC TEST VALUES
SCAN “NO GOOD”
I
SCAN “NO GOOD”
R
R
NO
NO
NO
YES
YES
YES
PROGRAM CHECKING/KNOB CHECK
LEAK TEST
RECORD LEAK TEST RESULT
CONSTRUCTION INSPECTION

## Slide 36
START OF INSPECTION 4
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
J
IS THE SERIAL AND MODEL NUMBER THE SAME?
PUNCTURE AND CHARACTERISTIC TEST
R
RECORD CHARAC TEST VALUES
DOES THE UNIT HAVE THE CORRECT MODEL LABEL AND BADGE? CORRECT MANUAL COMPLETE AND FRONT GRILLE?
PRINT “ERROR”
ARE THE VALUES WITHIN THE RANGE? DOES THE UNIT PASSED IN THE PUNCTURE TEST?
SCAN “NO GOOD”
K
SCAN “GOOD”
VISUAL INSPECTION
SCANNING OF MODEL & SERIAL NUMBER IN NAME PLATE AND BARCODE
SCAN AND RECORD: GOOD
END OF INSPECTION 4
SCAN NO GOOD
R
NO
NO
NO
YES
YES
YES

## Slide 37
START OF SFIS 5
END OF SFIS 5
1 BY 1 SCANNING OF CC CASE
CC CASE SERIAL NUMBER RECORDED
NO
IS IT THE CORRECT CC CASE FOR THE RUNNING MODEL? ARE THERE NO DAMAGES IN THE CC CASE?
IF INCORRECT CC CASE: PRINT “ERROR”
IF THERE ARE DAMAGES: SCAN NO GOOD, DAMAGED CC CASE
CHANGE THE CC CASE
YES
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
K
VISUAL INSPECTION
ARE ALL THE ACCESSORIES COMPLETE? (MANUAL, FRONT GRILLE, ETC. (DIFFERENT PER MODEL)
SCAN NO GOOD: LACKING
COMPLETION OF LACKING ACCESSORIES
YES
NO

## Slide 38: REPAIR
Notes:
1. Every decision should scan serial number first
2. If no good from previous scan, error will occur if scanned as good in the next one, only the scanner that tagged the unit as no good can change to good

## Slide 39
START OF REPAIR
SCANNING OF MODEL & SERIAL NUMBER
MODEL & SERIAL # RECORDED
R
SCAN FOR CATEGORY OF REPAIR
DOES THE REPAIR NEED A NEW PART?
REPAIR
IS IT A SAFETY PART?
SCAN THE NEW PART
NO
YES
BRING BACK TO THE MAIN LINE
END OF REPAIR
EVALUATE AT QC
DOES THE UNIT PASSED THE EVALUATION?
YES
YES
NO
NO
SCAN: REPAIR DONE (SPECIFIC REPAIR)
SCAN: REPAIR DONE (SPECIFIC REPAIR)
SCAN: REPAIR DONE (SPECIFIC REPAIR)
SCAN MODEL & SERIAL NUMBER
If repair was done, new data is added to the previous one, for history.
Repair option when bringing back to line

## Slide 40: MACHINE SPECIFICATION
Airtight Test
  Machine Name: Air Tight Tester Machine
  Company: MAICO (Matsushita Industrial Corp.)
  Specifications:
    Main Voltage: AC 100V
    Temperature: 40 OC
    Pipe Size: 3/8’(inch)
    Liquid or gas: Compressed High Air
    Test Pressure: 0.17 Mpa
    Cycle time: 20 second
  ELECTRICAL Part List
    Circuit Protector: BJS 30-3 AC100/200 30A
    AUX Relay: MY4N: 100VAC
    AUX Relay: HC4-L: DC24V
    Relay base HC4-L: PY14A
    Relay Base MY4N: PYF14A
    PLC: NAIS FP-1 C24
    Pressure Control: ALCO Control FF115-S5 BAR (6-30 BAR)
    Display Line Light: AC100-4L-SQUARE (4 Light)
    Control Box: KGN
    Push Button: 19530N and AH30-L
    Power Supply Unit: K50A-24
Gas Charging
  Machine Name: Refrigerant Charging Equipment
  Company: To-ou Kogyo Co., LTD
  Specifications:
    Main Voltage: 220
    Frequency: 60 Hz
    Consumption Supply: 4KVA
Puncture Testing
  Machine Name: Withstanding Voltage/Insulation Resistance Tester (TOS5300, TOS5301, TOS5302)
  Company: Kikusui Electronics Corp.
Characteristic Test
  Machine Name: AC/DC POWER HiTester 3334/3334-01
  Company: HIOKI
Vibration Test
  Machine Name: Vibration Meter VM-83
  Company: Rion Co., LTD

## Slide 41: MACHINE SPECIFICATION
Leak Test
  Machine Name: HLD5000 Halogen Leak Detector
  Company: INFICON
  Specifications:
    Physical Data:
      Lowest trigger level setting (for single gas probes): 1.0 g/a
      Lowest trigger level setting (for universal smart probes): 0.5 g/a
      Maximum trigger level setting: 50 g/a
      Measurement range (for single gas probes): 0-100 g/a
      Measurement range (for universal smart probes): 0-300 g/a
      Detectable refrigerants (single gas probes): R134a, R744, SF6
      Detectable refrigerants (universal smart probe): all halogens
      Response Time: 1s
      Time until ready for operation: 30s
      Recovery time: approx. 2s
      Gross leak recovery time: approx. 8s
    Electrical Data:
      Mains Supply Voltage: 100V…230V ± 10%, 50/60 Hz
      Power Consumption: <60VA
      In standby : <40VA
      Protection: IP 30
      Overvoltage category: II
      Gas flow at the intake: 320 sccm
Characteristic Test
  Machine Name: *
  Company: Tokyo Rikosha Co., LTD.
  SP-07305
  Specifications:
    *
Characteristic Test
  Machine Name: *
  Company: Crenserv Industrial Corp.
  SP-07305
  PLC Components List:
    Main board: Q312B
    PSU: QS1P
    CPU: Q01CPU
    Ethernet module: QJ71E71-100
    Serial Module: QJ71E71C24N-R2
    Ethernet Switch: jyd-5, 5 Ports
    Extension board: Q612B
    PSU: Q64PN
    DI module: QX40
    DO Module: QY10
    Analog input: Q68ADI
    HMI: GT2710-STBA